## Slide 1: Physics 2 – April 23, 2019
P3 Challenge – A 1.50 mol gas sample is compressed isobaricly from a volume of 0.300 m3 to 0.100 m3. The gas was initially at a temperature of 300 K.
1) Determine the Work done by the gas.
2) Determine the change in internal energy.
3) Determine the Heat for this process.
Today’s Objective:
  Heat Engines
Assignment:
  B.2 p33#32, 34-37
Agenda
  Heat Engines
  Refrigerators
  Efficiency
  Carnot Engine

## Slide 2: Heat Engines
The purpose of a heat engine is to capture thermal energy and transform it into mechanical energy.
The opposite is easy: Converting mechanical energy into thermal energy is often accomplished with friction.
From the laws of thermodynamics, we know that thermal energy flows from hot objects to cold objects. It is this thermal energy that a heat engine can capture.

## Slide 3: Heat Engines
Heat engines usually take the form of a gas within a cylinder with a piston.
The piston moves in response to state changes of the gas.
The piston can do mechanical work, thus completing the transformation to mechanical energy.
This is a typical car engine piston apparatus

## Slide 4: A Sample Heat Engine Cycle Visualized
Heat is added from a hot heat source (first image) QH
Gas expands doing mechanical work to lift M (second image) W
The gas is cooled isovolumetrically (third image)
Heat is expelled at lower temperature (fourth image) QC
The mass is replace and the cycle repeats QH = QC + W

## Slide 5: Refrigerators
The second law states heat will not naturally flow from a cold object to a hot object
But this transformation can be accomplished if a refrigerator does work on the system.
A refrigerator is a heat engine run backwards.

## Slide 6: Versions of the Second Law (Life’s not fair)
Clausius version:
It is impossible for thermal energy to flow from a cold object to a hot object without performing work.
Kelvin version:
In a cyclic process, it is impossible to completely convert heat into mechanical work.
Note, for the opposite: Mechanical work can be completely converted into heat.

## Slide 7: Engine Efficiency
Engine Efficiency, , is defined as:
That is, what percentage of the thermal energy extracted from the heat sink can be transformed into mechanical energy.
Any unconverted energy is vented to a cold sink as QC.
W = QH - QC

## Slide 8: Engine Efficiency
The second law requires that there is no such thing a 100% efficient engine.
The most efficient engine possible is called the Carnot engine
It is a limit on the efficiency of any engine operating between any two given temperatures.
So what is a Carnot engine?

## Slide 9: The Carnot Engine
Four stages of the Carnot cycle:
12 Isothermal compression, Qc at Tc leaves
  Heat expelled, Qc< 0
23 Adiabatic compression, increase T
34 Isothermal expansion QH at TH added
  Heat added, QH > 0
41 Adiabatic expansion, decrease T
W = |QH | – |QC |

## Slide 10: Carnot Efficiency (Derived) Part 1
Begin with entropy for the cycle:
  S =Q/T for both isothermal steps. (one positive , one negative )
  S=0 for the adiabatic steps.
  Total S is zero because entropy is a state function
0 = QH/TH – QC/TC Difference in entropy is zero.
QH/TH = QC/TC Set equal.
QH/QC = TH/TC Rearrange. QC/QH = TC/TH Flip.

## Slide 11: Carnot Efficiency (Derived) Part 2
QC/QH = TC/TH (from above)
 = W/QH Efficiency defined
 = (QH – QC)/QH Substitute from W = QH – QC
 = 1 – QC/QH Rearrange.
 = 1 – TC/TH Substitute from above.
 = 1 – TC/TH Result is the limit on efficiency.
Efficiency = 100% only if TC = 0 K or TH = . Both absurd.

## Slide 12: Other Engines – Stirling Engine

## Slide 13: Other Engines – Diesel Engine

## Slide 14: Other Engines – Otto Engine (Typical car engine)

## Slide 15: Refrigeration

## Slide 16: Exit Slip - Assignment
Exit Slip- Sketch the Carnot cycle on a PV diagram. Label the four stages with the type of process and expansion/compression.
What’s Due? (Pending assignments to complete.)
  p34#32, 34 -37
What’s Next? (How to prepare for the next day)
  Read 8.1 p314-326 about Energy Sources (Think about groups for presentations on the five sources: Fossil fuels, Wind, Hydroelectric, Nuclear, Solar)